## Slide 1
Pierdomenico Fiadino
The Telecommunications Research Center Vienna (ftw.)
Challenging Entropy-based Anomaly Detection
and Diagnosis in Cellular Networks
fiadino@ftw.at
http://userver.ftw.at/~fiadino

## Slide 2
MOTIVATION
111
Challenging Entropy-based Anomaly Detection and Diagnosis Slide #2
Today’s Internet is characterized by increasing complexity
Multiple network types (WiFi, cellular, FTTH, etc.)
Large scale and highly distributed services (CDNs)
Sophisticated and highly dynamic traffic patterns
Frequent anomalies involving specific sub-populations of users
Are the traditional Anomaly Detection (AD) approaches still able to cope with this complex scenario?
We challenge the applicability of Entropy-based Anomaly Detection in typical modern day scenarios by comparing it with a more complex Distribution-based detector.

## Slide 3
111
REAL-WORLD USE CASES
device-specific push/cloud services
?
?
?
?
?
RCATool: An Automatic Detection and Diagnosis Framework Slide #3
RCATool framework evaluated for 6 months in 2014 on operational cellular network (DNS traffic)
Many paradigmatic use-cases (events) have been collected
manufacturers
#DNS queries
operative systems
#DNS queries
DNS
server
requested hostnames (FQDN)
#DNS queries

## Slide 4
111
111
TWO ALTERNATIVE DETECTORS
Represent entire distribution as Entropy
Entropies captures the dispersion of the corresponding probability distribution
A change in traffic patterns induces a change (spike/notch) in the entropy of the relevant traffic feature
Challenging Entropy-based Anomaly Detection and Diagnosis Slide #4
Detector #1: Entropy-based
H(current) = 0.42
Entropy
current distribution
2015-08-18 08:00

## Slide 5
111
TWO ALTERNATIVE DETECTORS
Challenging Entropy-based Anomaly Detection and Diagnosis Slide #5
A more complex solution: consider whole empirical distribution of traffic features instead of just its entropy
Compute distance between distribution and a reference set of anomaly-free distributions (rapresenting normal behaviour)
Entropy normalized KL metric
Detector #2: Distribution-based
111
D(current) = 3
current distribution
reference distribution
Distribution distance metric
Kullback-Leibler divergence

## Slide 6
REAL-WORLD USE CASES
111
Challenging Entropy-based Anomaly Detection and Diagnosis Slide #6
 | Event #1 | Event #2
Start time | 9:00 | 12:00
Duration | 1 hour | 2 days
Devices | 10% | 5%
Back-off time | 5 seconds | 180 seconds
Manufacturer | Apple Inc. | Multiple (Samsung, HTC, ...)
O.S. | iOS 8.* | Android 4.*
Error flag | +5% time-outs | --
FQDN | OS-specific Top 3LD (push.apple.com) | OS-specific Top 3LD (mtalk.google.com)

## Slide 7
DNS TRAFFIC FEATURES
111
Challenging Entropy-based Anomaly Detection and Diagnosis Slide #7
DSN traffic features considered
Device related: manufacturer and OS
Service related: requested hostnames (FQDN)
Network performance related: status code of DNS resolver
Anomalies usually visible by observing DNS traffic
Event #1 (Apple)
Event #2 (Android)

## Slide 8
DETECTORS OUTPUT
111
Challenging Entropy-based Anomaly Detection and Diagnosis Slide #8
Entropy of relevant features is clearly altered
Easily detected by algoriths such as EWMA
Entropy is not clearly visible
EWMA fails to detect the whole duration of the anomaly
Detector #1: Entropy-based
Event #1 (Apple)
Event #2 (Android)

## Slide 9
DETECTORS OUTPUT
111
Challenging Entropy-based Anomaly Detection and Diagnosis Slide #9
Both event type exhibit a clear devergence from the normality reference
The whole duration of the anomaly is detected
Detector #2: Distribution-based
Event #1 (Apple)
Event #2 (Android)

## Slide 10
111
COMPARING PERFORMANCE
Event Type #1
Event Type #2
Entropy-based
detector
Distribution-based
detector
ROC Curves
RCATool: An Automatic Detection and Diagnosis Framework Slide #10

## Slide 11
CONCLUSION
111
Challenging Entropy-based Anomaly Detection and Diagnosis Slide #11
Entropy-based detectors are the most popular and largerly adopted, but they fail in coping with smaller-intensity – but still harmful – anomalies which are very common in modern-day networks

## Slide 12
Thank you for your attention 
Pierdomenico Fiadino
The Telecommunications Research Center of Vienna
http://userver.ftw.at/~fiadino
fiadino@ftw.at
http://www.ict-mplane.eu/

## Slide 13
backup slides...

## Slide 14
111
111
TRAFFIC FEATURE DISTRIBUTION
Challenging Entropy-based Anomaly Detection and Diagnosis Slide #14
manufacturer
number of DNS queries
Apple
Samsung
Huawei
HTC
LG
Distribution of DNS queries across device manufacturer
Devices affected by an anomaly induce a change in traffic feature distributions

## Slide 15
TWO ALTERNATIVE DETECTORS
111
Challenging Entropy-based Anomaly Detection and Diagnosis Slide #15
Key idea: detect abrupt changes in time series of empirical entropy of certain traffic features (i.e., descriptors).
Entropies captures the dispersion of the corresponding probability distribution
A change in traffic patterns induces a change (spike/notch) in the entropy of the relevant traffic feature
Detector #1: Entropy-based

## Slide 16
TWO ALTERNATIVE DETECTORS
111
Challenging Entropy-based Anomaly Detection and Diagnosis Slide #16
A more complex solution: consider whole empirical distribution of traffic features instead of just its entropy
Compute distance between distribution and a reference set of anomaly-free distributions (rapresenting normal behaviour)
Example of distance metric: normalized Kullback-Leibler
Kullback-Leibler divergence
Entropy normalized KL metric
Detector #2: Distribution-based