## Slide 1
Unraveling Internet-scale Services
from the Eyes of an Access Operator
Pierdomenico Fiadino, PhD
Talk @ Telefonica I+D
Barcelona, February 11th 2016

## Slide 2
111
$> whoami
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #2
Bari
Rome
Vienna
Computer Engineering (BSc and MSc degree)
2005 – 2010
Researcher (computer networks area)
2010 – 2015
PhD (Institute of Telecommunications)
2012 – 2015
Bari (Italy)
Rome (Italy)
Vienna (Austria)

## Slide 3
$> ls ~/projects | grep ”network monitoring and analysis”
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #3
2010 - 2012
Mobility studies (ITS)
leveraging cellular network monitoring
Collaborations: Austrian highway corporation, Telekom Austria (A1), Austrian civil engineering consultancy companies
Goals: study macro mobility on national-level
Identification of popular trajectories and O/D matrices
Inference of road traffic conditions
Identification of transport means
Vermobil
RoadCell

## Slide 4
111
Passive Measurements
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016 Slide #4
network operator
Streaming data-warehouse (SQL)
Network to geographical mobility
passive probe
network traces
devices
Access Network
Handovers
Location Area Updates
Calls/SMS
...
Signaling messages from
A/Gb/IuPS/IuCS
interfaces
test drives
Cell sequences on highways
test terminal

## Slide 5
From raw data to highway data
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #5

## Slide 6
From raw data to highway data
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #6

## Slide 7
From raw data to highway data
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #7

## Slide 8
From raw data to highway data
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #8

## Slide 9
Means of transport differentiation
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #9
Vienna
Vienna
Highway network:
Railway network:
Linz
Linz

## Slide 10
Means of transport differentiation
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #10
Legend
cell
transition
Linz
Vienna
St. Pölten
Amstetten
railway
highway

## Slide 11
From raw data to highway data
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #11

## Slide 12
$> ls ~/projects | grep ”network monitoring and analysis”
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #12
Darwin
2010 - 2012
2012 - 2015
Mobility studies (ITS)
leveraging cellular network monitoring
Internet traffic monitoring and analysis
Collaborations: Austrian highway corporation, Telekom Austria (A1), Austrian civil engineering consultancy companies
Goals: study macro mobility on national-level
Identification of popular trajectories and O/D matrices
Inference of road traffic conditions
Identification of transport means
Vermobil
RoadCell
Collaborations: Telcos, Universities, etc.
Goals: Web traffic classification, Internet traffic characterization (focus on popular applications), anomaly detection and diagnosis...
The topic of this talk!

## Slide 13
Passive Measurements
111
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...
Slide #13
network operator
internet
Streaming data-warehouse (SQL)
Characterization and Diagnosis
passive probe
network traces
devices
Access Network
HTTP tickets
DNS tickets
TCP-level statistics
...
Gn interface

## Slide 14
Simpler Web provisioning infrastructures
Traffic volume dominated by P2P applications
Rudimental monitoring tools and simpler problems
client
server
path
Rewinding the clock of the Internet to a decade ago...

## Slide 15
nowadays
Internet’s landscape
has drastically changed
P. Fiadino – PhD Defense – Deceber 10th, 2015...............
Slide #15
nowadays
Internet’s landscape
has drastically changed

## Slide 16
Latency
and bandwidth
sensitive
Complex Applications and Provisioning Systems
cloud platforms
online social networks
media streaming
Content Delivery Networks (CDN)
Need for sophisticated and highly distributed hosting infrastructures
Large
user-base
High traffic volume
optimize underlying network usage
increase users‘ Quality of Experience
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #16

## Slide 17
Content Delivery Networks and load balancing
client
Content
Servers
Local
DNS
Service
FEs
(3) Client resolves
Content server name
(1) Client requests content to FE
(4) Client requests content
(2) FE replies with content server name
Load-balancing through
DNS differentiation
Many organizations, ASes and FQDNs are involved in providing the service
CDN network
Other techniques: ANYCAST
Users dynamically redirected
Distributed FrontEnds (FEs)
Distributed Content Servers (replicas)
CDNs: pushing contents as close as possible to final users and deploy multiple replicas
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #17

## Slide 18
111
The Uphill Race to Network Monitoring & Analysis
The Internet is the first thing that humanity has built that humanity doesn't understand, the largest experiment in anarchy that we have ever had.
‘‘
Eric Schmidt
Alphabet Inc chairman
…but we miss the technology to understand what is happening in the network and to optimize its performance and utilization*
*especially when something goes wrong...
resource planning
content caching
traffic engineering
trend analysis
anomaly detection and diagnosis
...
Relevance for ISPs
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #18
Notes: Rimuoverla o alleggerirla,comuqneu andare piu veloce

## Slide 19
Research Questions
111
Learn how to track the Internet’s “Big Players”
service differentiation in large-scale operational networks
(in a cyphered-Internet)
Q1
Study their provisioning systems, load balancing dynamics and flow characteristics
characterization of normal operations and anomalous behaviors
Q2
Design algorithms for automatic detection and diagnosis of network anomalies
devise a more structured approach that facilitates the troubleshooting
Q3
My contributions in the filed of Network Traffic Monitoring and Analysis (nTMA)
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #19

## Slide 20
Data sources and tools
Active measurements
ping, traceroute
In-network passive measurements
operational networks, cellular and fixed-line
Distributed measurements
RIPE Atlas framework
GeoIP Datasets
MaxMind (<IP-AS> and <IP-Country> mappings)
Hybrid Measurements
Generate traffic and capture it with packet analyzers (Wireshark)
Metawin
(cellular network)
Tstat
(fixed-line network)
localhost> ping google.com
PING google.com (1.1.1.1) 56(84) bytes of data
64 bytes from google.com: icmp_seq=1 ttl=57 time=15.8ms
64 bytes from google.com: icmp_seq=2 ttl=57 time=11.9ms
devices
ISP network
Internet
Access Network
Streaming data-warehouse (SQL)
network traces
BigData analytics
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #20

## Slide 21
Research Questions
111
Learn how to track the Internet‘s “Big Players”
service differentiation in large-scale operational networks
(in a cyphered-Internet)
Q1
Study their provisioning systems, load balancing dynamics and flow characteristics
characterization of normal operations and anomalous behaviors
Q2
Design algorithms for automatic detection and diagnosis of network anomalies
devise a more structured approach that facilitates the troubleshooting
Q3
My contributions in the filed of Network Traffic Monitoring and Analysis (nTMA)
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #21

## Slide 22
Service differentiation through pattern matching
111
Example: Facebook regex (((|%.)(facebook.com|fbcdn.net))|((fbcdn|fbstatic)%.akamaihd.net))
URL: http://www.bbc.co.uk/...
Timestamp = 1400001684
Req. bytes = 172
Res. bytes = 420
Server IP = 1.1.1.1
[...]
HTTP ticket
^www\.google(\.[a-z]{2,3}){1,2}$
^www\.facebook\.com$
^www\.fbcdn\.net$
^www\.bbc\.(co\.uk|com)$
Google (search)
Facebook
Facebook
BBC
regular expressions
service
pattern matching
a
manually defined patterns
initial effort, but quite high stability
b
classify by pattern-matching
on requested URL
c
easy discovery of new popular services
d
allows association between server IP and service
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #22

## Slide 23
Leveraging DNS for encrypted protocols
resolve: www.youtube.com
A: <IP1,IP2,..>, TTL
A: <IP1,IP2,..>, TTL
resolve: www.facebook.com
client #1
client #2
DNS server
Passive probe
userID | FQDN | IP | start | end
user #1 | www.yt.com | 1.1.1.1 | 14041347 | 14041349
user #2 | www.fb.com | 2.2.2.2 | 14030424 | 14031288
... | ... | ... | ... | ...
local mapping
validity period (TTL)
    use passively collected DNS requests to dynamically map <services,serverIPs>
idea
2
every subsequent flow between a <user> and a <server_ip> in the validity period [validity_start:validity_end] are assigned to <FQDN>
the Fully Qualified Domain Names (FQDN) are assigned
to service with usual pattern matching (previous slide)
3
1
build a local mapping of <fqdn> and <server_ip>, with specific vality period, by observing passive traces
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #23

## Slide 24
Service Differentiation -- Summary
      INFOCOM 2013 Poster Session , IWCMC 2013, ACM SIGCOM 2014 Poster Session
publications
      Evaluation of HTTPTag (classification rate in operational cellular network)
      Long-term tracking capabilities of HTTPTag (antivirus definition updates and others)
      Mini-IPc: a simple IP-based classifier (evaluation and limitations)
      DNS extension for encrypted XMPP-based applications (e.g., WhatsApp)
other contributions (not shown)
      An on-line system for web traffic classification (HTTPTag) relying on headers
      An extension considering DNS traffic for encrypted protocols (HTTPTag2)
my main
contributions
designed, implemented and deployed in operational cellular networks
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #24

## Slide 25
Research Questions
111
Learn how to track the Internet‘s „Big Players“
service differentiation in large-scale operational networks
(in a cyphered-Internet)
Q1
Study their provisioning systems, flow characteristics and load balancing dynamics
characterization of normal operations and anomalous behaviors
Q2
Design algorithms for automatic detection and diagnosis of network anomalies
devise a more structured approach that facilitates the troubleshooting
Q3
My contributions in the filed of Network Traffic Monitoring and Analysis (nTMA)
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #25

## Slide 26
Internet-scale applications: three study cases
a
Hosting infrastructure discovery
Server IPs, AS/CDN/companies involved, geographical (MaxMind) and topological (RTT) positioning
b
Study of Temporal Dynamic Characteristics
Unveil traffic seasonality, load balancing policies by observing IP addresses and minRTT
c
Flow Characteristics and QoE Implications
Average throughput, QoE-based KPIs (e.g., video bitrate/throughput ration)
Characterization of popular applications
(chosen according to their relevance, generated traffic volume and user-base size)
during their normal operations
Online Social Network
cellular dataset
Video Streaming
cellular and fixed-line dataset
Instant Messaging
cellular dataset
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #26

## Slide 27
A. Hosting Infrastructure (Facebook case)
37.2%
Austria (same country)
12.7%
Ireland
2.1%
Germany
1.1%
USA
46.3%
Rest of Europe
99% traffic from
within Europe
1
Strong content localization
2
Akamai datacenters in Europe play biggest role
3
ISP caching: local and neighboring countries
Geographical diversity
FB. traffic sources to Austria
(cellular network)
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #27

## Slide 28
A. Hosting Infrastructure (where are the caches?)
111
Distribution of min RTT per service and per hosting organization (num. flows weighted)
Facebook example
min RTT approximate propagation delay
Knees in the distributions correspond to different hosting locations
AkamaiAS: very short RTT
(highly distributed and close to final users)
Intuitively ISPs (Local ISP and Deutsche Telekom) have small geographical diversity
Akamai
Facebook AS
Local ISP
Deutsche T.
TeliaNet
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #28

## Slide 29
111
B. Temporal Patterns: heat maps visualization
minRTT Heat-map evolution
(concentration of flows in different locations/datacenters)
Google CDN (Youtube) uses load balancing
contents from different locations depending on time/load
Google CDN presents marked RTT shifts
daily periodic patterns and a stable hosting locations
minRTT of Youtube flows (Google CDN)
Heatmaps for unveiling involved locations/datacenters and their inter-play
Results from operational cellular network (millions of users)
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #29

## Slide 30
B. Temporal Patterns: heat map visualization
uniform settings
  Count flow numbers/volume for every IP
1
  Cumulate counters per unit of time (e.g. 1h)
2
  Calculate distributions per time-bin
3
  Compare distributions (Kullback-Leibler)
4
  Plot comparisons on heatmap (logscale)
5
      A powerful heatmap-like tool for visualizing temporal patterns
      Discover temporal patterns and (ir)regularities in distribution timeseries
Temporal Similarity Plot (TSP)
How to build a TSP
Long-term distribution of flows across Akamai subnets (Facebook case)
as observed in a cellular networks (millions of users)
week 1
week 2
week 3
week 4
week 2
week 3
week 4
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #30

## Slide 31
111
C. Flow Characteristics and QoE (WhatsApp)
Users tolerate transfers (in chat apps) of up to 20 seconds with good experience
Threshold of 40 seconds discriminates good and bad experience
The score is independent of the flow size (e.g., independent of video quality)
Laboratory Experiments
Results
media transfer in IMM
Distribution of download time (as seen in large-scalepassive traces)
[video exchange in chat application]
From laboratory experiment to operational networks
(large scale measurements)
40% flows last less than 20s (good)
60% flows last less than 40s (acceptable)
35% flows are badly/very badly perceived
Map network characteristics to user assigned score (from 1 to 5)
Laboratory experiments with network controlled environments and real users
The score is independent of the flow size (e.g., independent of video quality)
Laboratory Experiments
QoE models
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #31
Notes: Remove details on model and just put the conclusions and of the model and how they apply

## Slide 32
Internet-scale applications: three study cases
a
Hosting infrastructure discovery
Server IPs, AS/CDN/companies involved, geographical (MaxMind) and topological (RTT) positioning
b
Study of Temporal Dynamic Characteristics
Unveil traffic seasonality, load balancing policies by observing IP addresses and minRTT
c
Flow Characteristics and QoE Implications
Average throughput, QoE-based KPIs (e.g., video bitrate/throughput ration)
Characterization of popular applications
(chosen according to their relevance, generated traffic volume and user-base size)
during their normal operations
Online Social Network
cellular dataset
Video Streaming
cellular and fixed-line dataset
Instant Messaging
cellular dataset
d
Anomalies!
Outages, pattern changes with negative implications
!
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #32

## Slide 33
Facebook traffic and CDN inter-play anomalies
srv IP
constant share of traffic among CDNs
Facebook AS and Akamai lead in terms of flow num.
Akamai deploys the largest number of IP per time unit
flows
Total
Akamai
Facebook AS
Local ISP
Deutsche T.
TeliaNet
Anomalous events (frequent)
Traffic drop in Akamai AS (drop in number of served flows, active IPs)
Deutsche Telekom and TeliaNet deploy back-up machines (increase number of active IPs) and together take over the role of Akamai
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #33

## Slide 34
Facebook traffic and CDN inter-play
111
Deutsche Telekom
TeliaNet
Local operator
Akamai
p2p
(free)
c2p
($$$)
c2p
($$$)
:(
AS
AS
AS
AS
No impacts for users. Why should operators care?
Potential economical loss for ISP
CAIDA’s AS-relations dataset
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #34

## Slide 35
Change of CDN policies and QoE degradation
111
 |  | 5-May |  | 6-May |  | 7-May |  | 8-May |  | 9-May |  | 10-May | 
SUBNET | NAME with AIRPORT code | #flow | Thr avg | #flow | Thr avg | #flow | Thr avg | #flow | Tru avg | #flow | Tru avg | #flow | Tru avg
173.194.18 | fra02s08.c.youtube.com | -1 | -1 | -1 | -1 | -1 | -1 | 6139 | 368.93 | 6266 | 298.4 | 5389 | 228.76
173.194.19 | fra02s15.c.youtube.com | -1 | -1 | -1 | -1 | -1 | -1 | 9940 | 258.18 | 12893 | 196.06 | 7012 | 166.48
173.194.2 | mil01s12.c.youtube.com | 17054 | 1333.46 | 15470 | 1276.31 | 13655 | 1259.63 | 14186 | 1296.07 | 12616 | 1197.64 | 13860 | 1338.63
173.194.20 | par08s06.c.youtube.com | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
173.194.208 | par08s06.c.youtube.com | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | 487 | 414.63 | 71 | 711.54
173.194.5 | lhr14s08.c.youtube.com | 449 | 1819.57 | 283 | 1658.45 | -1 | -1 | 3470 | 937.18 | 4222 | 1025.49 | 6191 | 1166.08
173.194.6 | fra07s13.c.youtube.com | -1 | -1 | -1 | -1 | -1 | -1 | 4924 | 412.17 | 8749 | 331.14 | 7224 | 318.83
173.194.62 | fra07s19.c.youtube.com | -1 | -1 | -1 | -1 | -1 | -1 | 6160 | 325.82 | 6877 | 248.39 | 6108 | 274.55
173.194.9 | par03s06.c.youtube.com | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | 87 | 355.1 | -1 | -1
208.117.236 | par03x04.c.youtube.com | 179 | 164.18 | 4250 | 540.16 | 957 | 496.91 | -1 | -1 | -1 | -1 | -1 | -1
208.117.248 | mia02s11.c.youtube.com | -1 | -1 | 77 | 552 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
208.117.250 | ams09x06.c.youtube.com | 41430 | 679 | 49437 | 656.39 | 57675 | 653.81 | 567 | 906.65 | -1 | -1 | -1 | -1
208.117.252 | dfw06x02.c.youtube.com | -1 | -1 | 51 | 285.63 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
208.117.254 | fra07x03.c.youtube.com | 838 | 667.29 | 2130 | 852.53 | -1 | -1 | 465 | 606.1 | 126 | 1146.87 | 1033 | 1379.76
74.125.105 | lhr22s16.c.youtube.com | 1829 | 1551.78 | 1655 | 1185.94 | 3957 | 942.47 | 3454 | 990.64 | 4116 | 1061.72 | 7657 | 1126.83
74.125.13 | zrh04s03.c.youtube.com | 719 | 1074.15 | 499 | 2264.09 | 82 | 1302.03 | -1 | -1 | -1 | -1 | -1 | -1
74.125.14 | mil02s01.c.youtube.com | 48366 | 1234.82 | 37968 | 1253.01 | 37182 | 1162.85 | 47844 | 1298.45 | 52594 | 1226.85 | 37755 | 1143.37
74.125.216 | bru02t11.c.youtube.com | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
74.125.218 | fra07t13.c.youtube.com | 8697 | 1355.33 | 12579 | 1338.71 | 8560 | 1239 | 11469 | 1256.32 | 11633 | 1292.58 | 10320 | 1276.33
74.125.4 | lhr22s11.c.youtube.com | 1496 | 1846.25 | 2488 | 1034.78 | 4146 | 1363.63 | -1 | -1 | -1 | -1 | -1 | -1
74.125.99 | fra07s03.c.youtube.com | -1 | -1 | -1 | -1 | -1 | -1 | 4221 | 187.84 | 4913 | 189.64 | 2461 | 136.63
Requestes served by different /24 subnets
..which correspond to different data centers
The Youtube case
Measurements from a single vantage poing (fixed-line)
flows shifted
flows shifted
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #35

## Slide 36
Change of CDN policies and QoE degradation
111
CDFs at peak hours (9pm – 11pm)
before and after change in cache selection policy
Before: more than70% of flows at ~800Kbps
After: more than 70% of flows at ~448Kbps
Avg. Downlink Rate and QoE (360p)
MOS = Mean Opinion Score
(1-month field trial, 40 users)
Google‘s cache selection policies might be sub-optimal!
Loss of 1 QoE point (MOS from 4 to 3): users noticed and complained to customer care
Throughput does not tell the whole story: additional QoE KPIs have been studied (β parameter)
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #36

## Slide 37
Internet-scale services characterization - summary
      Comparison of hosting infrastructure approaches (more details)
      Details on Internet Big Players (“who is hosting who”)
      Facebook flow characteristics
      Facebook anomalies inspected through Temporal Similarity Plots (TSPs)
      Facebook anomalies, characterization of two global outages
      YouTube traffic differences in cellular and fixed-line networks
      YouTube extended QoE study
      WhatsApp reverse engineering of naming scheme (hybrid measurements)
      WhatsApp traffic characteristics depending on terminals’ Operating Systems
my other contributions (not shown)
      Extensive characterization of popular hosting infrastructures
      Combination of heterogeneous data source (i.e., passive, active, geoIP, etc.)
      Methodology for studying and visualizing temporal evolutions (TSP for CDNs)
      Studies in operational networks (thousands/millions of users) and results with high statistical relevance
my main
contributions
      ITC 2013 B.P.A. PAM 2014 Poster session, IWCM 2014, IWCM 2014, EuCNC 2014, CNSM 2014, IEEE TNSM 2014, ACM SIGCOMM 2014 Poster session, WD 2014 B.P.A. Runner Up,
      TMA 2015, IFIP Networking 2015, EuCNC 2015, IWCM 2015
publications
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #37

## Slide 38
Research Questions
111
Learn how to track the Internet‘s „Big Players“
service differentiation in large-scale operational networks
(in a cyphered-Internet)
Q1
Study their provisioning systems, load balancing dynamics and flow characteristics
characterization of normal operations and anomalous behaviors
Q2
Design algorithms for automatic detection and diagnosis of network anomalies
devise a more structured approach that facilitates the troubleshooting
Q3
My contributions in the filed of Network Traffic Monitoring and Analysis (nTMA)
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #38

## Slide 39
Diagnosis framework at a glimpse
111
Symptomatic Signal Extraction
Diagnostic
Signal Extraction
Change Detection Module
Change Detection Module
Network
Traces
(traffic features)
Diagnosis Module
Symptom query_cnt
Diagnostic manufacture
Diagnostic operative_sys
Diagnostic FQDN
Granularity 30 minutes
Warning_start 2015-02-14
Alarm_start 2015-02-14
alarm_end 2015-02-14
Warning_end 2015-02-14
Symptom query_cnt
Diagnostic manufacture
Diagnostic operative_sys
Diagnostic FQDN
Granularity 30 minutes
Warning_start 2015-02-14
Alarm_start 2015-02-14
alarm_end 2015-02-14
Warning_end 2015-02-14
Symptom query_cnt
Diagnostic manufacture
Diagnostic operative_sys
Diagnostic FQDN
Granularity 30 minutes
Warning_start 2015-02-14
Alarm_start 2015-02-14
alarm_end 2015-02-14
Warning_end 2015-02-14
Symptom query_cnt
Diagnostic manufacture
Diagnostic operative_sys
Diagnostic FQDN
Granularity 30 minutes
Warning_start 2015-02-14
Alarm_start 2015-02-14
alarm_end 2015-02-14
Warning_end 2015-02-14
Symptom query_cnt
Diagnostic manufacture
Diagnostic operative_sys
Diagnostic FQDN
Granularity 30 minutes
Warning_start 2015-02-14
Alarm_start 2015-02-14
alarm_end 2015-02-14
Warning_end 2015-02-14
Event Reports
passively collected
(e.g., from a mobile network core)
statistical content of diagnostic-symptomatic traffic features
probability distribution-based algorithm
state management, classification, correlation
provide support in troubleshooting of anomalous events
key idea
1
symptomatic signals
notify presence of anomalous state
diagnostic signals
provide context for diagnosis
distinguish between:
key idea
2
observe significant changes in multiple traffic features
key idea
3
keep status of changes, classify and coordinate
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #39

## Slide 40
Stage #1: Signal Extraction
Symptomatic Signals
describe statistical content of traffic features (e.g., distributions)
experimented with DNS tickets and video flows monitoring
Signals
Diagnostic Signals
    QoE-related anomalies (e.g., YouTube/Google)
    (degradation of QoE-related KPIs)
Network statistics that indicate the presence of anomalies (when they change)
Their change does not indicate presence of anomalies, but support troubleshooting
    QoE-related anomalies (e.g., YouTube/Google)
    (CDN settings, server IPs, RTT, etc.)
example
example
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #40

## Slide 41
Traffic Feature Distributions
111
Throughput bins (decreasing)
number of flows
>4Mbps
2-3Mbps
3-4 Mbps
1-2Mbps
Empirical distribution of flows across throuput ranges (binning)
Change in traffic patterns induce shifts in the distributions of the relevant traffic features
3-4 Mbps
Overall decrease of average throughput
(YouTube use case...)
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #41

## Slide 42
Stage #2: Change Detection
111
Entropy normalized KL metric
Distribution-based detector
Df(ti) = 3
current distribution at ti
reference distribution r
Distribution distance metric
Kullback-Leibler divergence
Consider whole empirical distribution
instead of just its entropy (as usually done)
Compute distance between distribution and normality reference
i.e. a set of historical anomaly-free distributions
Self-adapting sliding window algorithm for reference identification
my extension to the algorithm (originally based on simple sliding window mechanism)
Measures how different current distribution is from normality
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #42

## Slide 43
β parameter (QoE-based KPI) timeseries
(threshold based detection)
Distribution of flow count per throughput bins
(distribution-based detection)
Youtube QoE anomaly: Symptomatic Signals
Average download throughput change
Performance degradation
Unacceptable
β paramenter
(<1.25, lab experiments)
QoE impairments
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #43

## Slide 44
Youtube QoE anomaly: Diagnostic Signals
Distribution of flows across server IPs
Distribution of flows across remote elab. time
Distribution of flows across external RTT bins
Distribution of flows across internal RTT bins
server IPs
change
elaboration time change
new servers are involved
new servers are under-dimensioned?
(also possible congestion)
external RTT change
possible congestion?
NO change internal RTT
external cause
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #44

## Slide 45
Stage #3: Diagnosis Module (anomaly classification)
111
Supervised classification techniques
Classify detected anomalies (assign event lable)
Enrich final event reporting and support troubleshooting
Support Signal Correlation through ML
Evaluation on synthetic dataset (from real DNS anomaly templates)
Several tested algorithms
(SVN, NB, DT, RF, MLP)
C4.5 (Decision Tree) best performing*
Datasets includes detector outputs as features
*Considering feature selection approaches
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #45

## Slide 46
Stage #3: Diagnosis Module (state management)
111
Change Detection: from state-less to state-full
Add “inertia” to the system to track evolution of events
Keep states independently for each signal
State machine(s)
Normal
fr = 0
Warning
0 < fr < th
Anomaly
fr ≥ th
More robust in presence of flipping detector output
Allows definition of
event-lifecycle
Supports better reporting
(especially long-term events)
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #46
Notes: Dire meno dettagli su state machine che e‘ chiaro....

## Slide 47
Diagnosis Module: event reporting
Event #123456 {Gran. 15 minutes}
Type 1
-----------------------------------
Symptoms:
* beta [0.75,+][1.25,-]
* throughput [4Mbps,+][8Mbps,-]
Correlated diagnostic signals:
* servers [AS2,+][AS1,-]
* external RTT [100ms,+][80ms,-]
* elaboration t. [50ms,+] [20ms,-]
Uncorrelated diagnostic signals:
* internal RTT […]
-----------------------------------
Timestamps:
Warning_start 2015-02-14 19:00
Alarm_start 2015-02-14 19:15
Alarm_end 2015-02-14 22:45
Warning_end 2015-02-14 23:00
decrease of throughput and beta
new servers
with higher RTT and elaboration time
internal RTT unchanged (external problem)
at peak time
(underdimensioned servers)
event ID and type
(ML label)
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #47

## Slide 48
Anomaly Detection and Diagnosis -- Summary
      Study on entropy-based detectors and limitations
      Distribution-based detectors applied on Facebook anomalies
      Generation of synthetic traffic and anomaly injection
      Comparison of entropy-based detectors against distribution-based
      Novel Reference Identification Algorithm
      Extended evaluation of distribution-based detectors on DNS anomalies (focusing on detection capabilities depending on anomaly-intensity)
my other contributions (not shown)
      Study of many anomaly use cases (spanning different classes and network trace types)
      Extension of a distribution-based detector system with a self-adapting reference identification mechanism
      Design of a framework for parallel analysis of traffic features/signals
      Machine Learning techniques for automatic classification of anomalies
      Human-readable event reporting
my main
contributions
      IWCM 2014, ITC 201, CoNEXT 2014 Poster session
      ACM SIGCOMM 2015 Poster ACM Student Research Competition - Runner Up
      IWCMC 2015, ITC 2015, IEEE ComMag 2015 (to appear), JSAC 2015 (submitted)
publications
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #48

## Slide 49
Conclusions (and open topics for future research)
111
Internet service differentiation
Rely on HTTP/DNS monitoring and manual definition of regular expression
1
  Technique for classification of “big players” in a cyphered Internet
to-do
  More scalable and less manual
contribution
Extensive characterization of Internet-scale services
Investigating hosting infrastructure, geo-topological diversity, flow characteristics and QoE
2
  Structured methodology and
  valuable results from real networks
to-do
  Continue the characterization efforts, tackle new applications and patterns
contribution
Large-scale anomaly detection
Powerful distribution-based algorithm
3
  Application on CDN-related issue and reference identification algo.
to-do
  Concurrent anomalies
contribution
Towards Automatic Diagnosis of Anomalies
Supervised classification techniques, state management and automatic reporting
4
  Human-readable anomaly description to support troubleshooting
to-do
  Iterative/Distributed Diagnosis
  (first, promising, results!)
contribution
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #49

## Slide 50
Thank you for your attention!
      IWCM 2014 [2] (Distribution-based techniques, exploratory study)
      ITC 2014 (Distribution-based techniques applied on Facebook and YouTube anomalies)
      CoNEXT 2014 Poster session (DNS anomalies and entropy-based detectors)
      ACM SIGCOMM 2015 Poster (Limitations of entropy-based detectors) ACM Student Research Competition - Runner Up
      IWCMC 2015 (Diagnosis framework, preliminary study applying entropy detectors)
      ITC 2015 (Diagnosis framework applied on DNS anomalies)
      IEEE ComMag 2015 (to appear, Diagnosis framework in mPlane)
      JSAC 2015 (submitted, Diagnosis framework extended, YouTube experiments and ML)
Q3
Anomaly Detection
And Diagnosis
      ITC 2013 (Internet’s big player, extended characterization) B.P.A.
      PAM 2014 Poster session (Internet’s big players)
      IWCM 2014 [1] (Facebook characterization)
      IWCM 2014 [2] (YouTube anomaly, preliminary study)
      EuCNC 2014 (YouTube characterization, cellular vs fixed line)
      CNSM 2014 (YouTube characterization and QoE implications)
      IEEE TNSM 2014 (YouTube anomaly study, extended)
      ACM SIGCOMM 2014 Poster session (WhatsApp characterization)
      WD 2014 (Youtube caching strategies) B.P.A. Runner Up
      TMA 2015 (WhatsApp characterization, extended)
      IFIP Networking 2015 (Characterization of traffic from online social networks)
      EuCNC 2015 (QoE in online social networks)
      IWCM 2015 (QoE in online social networks, extended)
Q2
Characterization of traffic from popular Internet-scale services
      INFOCOM 2013 Poster Session (HTTP pattern-matching classification)
      IWCMC 2013 (IP-based classifier)
      ACM SIGCOMM 2014 Poster Session (DNS extension for encrypted protocols)
Q1
HTTP(S) Classification
publications

## Slide 51
backup slides

## Slide 52
Passive Measurements
111
network operator
internet
Streaming data-warehouse (SQL)
Characterization and Diagnosis
passive probe
network traces
devices
Access Network
HTTP tickets
DNS tickets
TCP-level statistics
...
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #52

## Slide 53
What to do next: Iterative Diagnosis
111
Capture
(active, passive, hybrid)
Import & Pre-process
(signal extraction)
Detect Changes
Iterative Diagnosis
Continuous Reporting
Set-up additional measurements (active/passive)
Capture
(passive)
Diagnosis
Sequential Diagnosis Scheme
  Effective in most scenarios.
  Mostly based on passive traces.
  Tested in operational networks (e.g., DNS anomalies)
  However, it might not be enough to diagnose probles outside operator‘s boundaries (sometimes)....
Iterative Diagnosis Scheme
  Set-up existing measurements and/or access existing ones.
  Distributed Vantage Points (federated measurement architecture)
  More flexible time-granularity management

## Slide 54
Distributed/Hybrid Measurement scheme
111
reasoner
repository
client
client
Passive
probe
Active
probe
data
control
access link
peering link
Internet
eXchange
Point
...
IXP
A
P
A
A
P
P

## Slide 55
Iterative Diagnosis Graph
Youtube flow throughput distribution change
drop in QoE-related KPIs?
device/OS related issue?
extrat dominant
device/OS type
device/soft issue
internal ISP diagnosis
ISP issue
path congestion events?
inter-AS path issue
CDN load balancing?
path congestion events?
server problems?
server issues
No
Yes
Yes
Yes
Yes
Yes
No
No
No
No
1
2
3
4
5

## Slide 56
Content Delivery Networks and load balancing
client
Content
Servers
Local
DNS
Service
FEs
(3) Client
resolves
content
server name
(1) Client requests content to FE
(4) Client requests content
(2) FE replies with content server name
Architecture
Workflow
Front-end
(FE)
Ingress
Router
Egress
Router
CDN Network
downstream
AS path
client
upstream
AS path
?
contents
  Front-end servers handle user requests
  Located at multiple A.S.
  Users are dinamically redirected
  Load-balancing through DNS differentiation
Many organizations, ASes and FQDNs are involved in providing the service

## Slide 57
Internet Big Players (Hosting and Services)
Services & hosting organizations
a
Different services hosted by multiple organizations
c
Non-cached Google/Youtube content exclusively hosted by Google.
Akamai EU hosts a large share of Facebook, Apple, Windows
Most IP of top services hosted by Google and Akamai
b
d
a
b
d
e
f
h
i
j
k
m,n,o
g
l
Hotmail
Google
Akamai EU
Limelight
Web Hoster
Facebook
Level 3
Youtube AS1
Youtube AS2
Apple
Microsoft
ISPs

## Slide 58
Internet Big Players (Hosting Companies)
Where the traffic is flowing from: an ISP perspective
Chart: 
| ISP | Google CDN | Akamai | Limelight | Lease Web | Others (e.g. Amazon)
Volume | 29 | 16 | 12 | 10 | 6 | 27
a
Association IP-AS
b
Few CDNs dominate Internet landscape
c
d
Top 4 host 40% of contents
Google CDN, Akamai, Limelight, LeaseWeb
Content caching at ISP
depending on vantage point
CDN
Google
Akamai
Limelight
LeaseWeb
#IPv4
#AS
#/24
~660k
~3.5M
~110K
~480K
8
22
8
3
~2.5K
~14K
~400
~1.8K
Cellular network, 1Ms users, 2014

## Slide 59
Visualization of temporal patterns
111
      A powerful heatmap-like tool for visualizing temporal patterns
      Discover temporal patterns and (ir)regularities in distribution timeseries
Temporal Similarity Plot (TSP)

## Slide 60
Temporal Dynamics: IP utilization per hour
Unique IPs per hour
Cumulative number of IPs
Number of flows per hour
a
Number of single IPs/hour providing HTTP services vary during day
From few 10s to 1000s different IP addresses per day
b
Google Search, YouTube and Facebook domanite the IP space
Because of their largerger volume and user base
c
Facebook is the most IP-distributed service (thanks to Akamai)
More than 2000 different IPs/day
d
Some services (e.g., AVS1) provisioned by very stable delivery infrastructure
Negligible changes in IP addresses active over the day

## Slide 61
Temporal Dynamics: IP utilization per hour
Facebook IPs
Windows Update IPs
Facebook
MS Windows Updates
Apple‘s iTunes and App Store
a
Different subnets of the CDNs are more dynamic than others
b
Akamai flows are serverd from very dynamically changing locations
Akamai places machines in operators‘ networks
c
``on demand´´ provisioning servers: Akmai‘s CDN philosophy
Akamai is among the most distributed and dynamic CDNs
d
Akamai flows are, a-priori, more difficult to track using servers Ips
It‘s extremely hard to track Akamai-based services by operators

## Slide 62
YouTube: cellular vs fixed-line (addressing space)
Comparing YouTube characteristics from two different perspectives
Fixed-line dataset (1000s customers)
1
Cellular dataset (1Ms customers)
2
3 Google Autonomous Systems
3600 IP addresses
100 networks/24
One of the two Google AS (spanning two /16) plays major role
3 Google Autonomous Systems
2000 IP addresses
63 networks/24
Local ISP AS (spanning one /16) plays an important role, serving 70% of flows!
Distribution of Youtube flows in the IPv4 addressing space (fixed-line vs cellular)

## Slide 63
YouTube: cellular vs fixed-line (flow characteristics)
Comparing YouTube characteristics from two different perspectives
Fixed-line dataset (1000s customers)
1
Cellular dataset (1Ms customers)
2
More than 15% flows achieve >2Mbps
Throughput governed by video bit-rate (not access technology!)
More than 15% flows achieve >2Mbps
Throughput governed by video bit-rate (not access technology!)
Highest througput from local ISP
Advantage of caching

## Slide 64
YouTube: cellular vs fixed-line (IP activity)
111
Comparing YouTube characteristics from two different perspectives
Fixed-line dataset (1000s customers)
1
Cellular dataset (1Ms customers)
2
Up to 700 IPs active at peak times
Load balancing depending on time of the day (very evident)
Up to 700 IPs active at peak times
Load balancing depending on time of the day (slightly less evident)
Local IPs are always on
More predictable dynamics (long-run)

## Slide 65
A. Hosting Infrastructure (Facebook case)
Number of IP addresses per A.S.
Share of flows per A.S.
b
Akamai plays a key role
50% of flowss and 2600 IP addresses
a
Akamai, Facebook AS, Tinet, CWW and neighbor operators
main involved ASses
c
Local and neighbor operators
caches
Topological diversity

## Slide 66
A. Hosting Infrastructure (Facebook case)
111
minumum RTT for all server IPs
minimum RTT for top hosting A.S.
a
minnRTT approximate delay
Knees in the distributions correspond to hosting locations
c
Facebook AS: three knees (Ireland
+ locations in USA through local IXP)
Akamai AS: very short RTT (highly distributed and close to final users)
Intuitively network operators have small geographical diversity
b
d

## Slide 67
A better QoE Key Performance Indicator (KPI)
111
  Throughput alone does not give information of user‘s perceived experience
  Correlate it with Video Bit Rate
Idea
  Average Download Throughput
ADT
  Video Bit Rate
VBR
β = ADT/VBR
metric reflecting user experience
  if (ADT<VBR) then low β and video stallings
  hence bad QoE
β-parameter vs. video stallings
High QoE (MOS>4) with β>1.25
No stallings
with β>1.25
from LAB tests

## Slide 68
DNS anomalies: the mobile operators´ plague
111
device-specific push/cloud services
manufacturers
#DNS queries
Operating systems
#DNS queries
DNS
server
requested hostnames (FQDN)
#DNS queries
?
?
?
?
?
Device-specific anomalies affecting sub-populations
Observed multiple instances in few months
Impacting operator-managed DNS servers and signaling plane

## Slide 69
Traffic Feature Distributions
111
manufacturers
number of DNS queries
Apple
Samsung
Huawei
HTC
LG
Distribution of DNS queries across device manufacturer
Devices affected by an anomaly induce a change in traffic feature distributions
Pierdomenico Fiadino – Barcelona, Feb. 11th 2016...............
Slide #69

## Slide 70
Detection Module
111
signal extr.
signal extr.
change
detection
change
detection
traces
diagnosis
Based on anomaly detection tool(s) from previous works, improved
Improved distribution-based with new reference identification algorithm
Key module for the whole framework
Tested two alternative detection strategies
Entropy-based and distribution-based

## Slide 71
Two Alternative Detectors
111
111
Hf(t0) = 0.42
Entropy
feature f distribution at t0
2015-08-18 08:00
Represent entiro distribution as Entropy
First tested detector: Entropy-based
Entropy captures the dispersion of the corresponding distribution
A change in traffic patterns induces a change (spike/notch) in the entropy of the relevant traffic feature

## Slide 72
Two examples of DNS events
111
P. Fiadino – PhD Defense – Deceber 10th, 2015...............
Slide #72
 | Event #1 | Event #2
Start time | 9:00 | 12:00
Duration | 1 hour | 2 days
Devices | 10% | 5%
Back-off time | 5 seconds | 180 seconds
Manufacturer | Apple Inc. | Multiple (Samsung, HTC, ...)
O.S. | iOS 8.* | Android 4.*
Error flag | +5% time-outs | --
FQDN | OS-specific Top 3LD (push.apple.com) | OS-specific Top 3LD (mtalk.google.com)

## Slide 73
Detectors Output
111
Detector #1: Entropy-based
  Entropy of relevant features is clearly altered
  Easily detectable by change-point-detection algorithms (e.g., EWMA)
  Entropies are not clearly altered
  EWMA fails in detecting the whole duration of the anomaly
DNS event #1 (Apple)
DNS event #2 (Android)

## Slide 74
Detectors Output
111
Detector #2: Distribution-based
DNS event #1 (Apple)
DNS event #2 (Android)
  Both events exhibit a clear divergence from normality reference
  The whole duration of the anomaly is detected

## Slide 75
Comparing other detection solutions
111
Event Type #1
Event Type #2
(legacy)
Entropy-based
detector
(endorsed)
Distribution-based
detector
ROC Curves

## Slide 76
Diagnosis Module (DNS anomaly reporting)
Event #123456 {Gran. 30 minutes}
Type 1
-----------------------------------
Symptoms:
* query_cnt [10,+][1,-]
Correlated diagnostic signals:
* manufacturer [Samsung,+]
* operative_sys [Android 4.1.2,+]
* FQDN [youcloud.com,+]
Uncorrelated diagnostic signals:
* error code […]
* APN […]
-----------------------------------
Timestamps:
Warning_start 2015-02-14 13:00
Alarm_start 2015-02-14 13:30
Alarm_end 2015-02-16 11:00
Warning_end 2015-02-16 12:00
increase of users executing
1 query / 3 minuties
Samsung users running Android 4.1.2, resolving youcloud.com
APN independent, error code distribution is not impacted
for almost 2 days
event ID and type
(ML label)

## Slide 77
Revealing WhatsApp´s Hosting Infrastructure
111
386 IP adresses used by Whatsapp (chat and media)
All in AS36351 (Softlayer)
Service/AS | #IPs | # /24 | # /16 | # /8
WhatsApp | 386 | 51 | 30 | 24
SoftLayer (AS36351) | 1364480 | 5330 | 106 | 42

## Slide 78
Revealing WhatsApp Hosting Infrastructure
111
Localization of servers through MaxMind and minimum RTT
  400 IP addresses observed
  all in Softlayer AS
1
  MaxMind-located in:
    Houston
    Dallas
2
  2 seps in RTT distribution
    106 ms
    114 ms
3
geographical localization
topological localization

## Slide 79
Revealing Whatsapp Hosting Infrastructure
111
IP addresses activity
at least 200 IPs are active at any time of the day
150 IPs ``always on´´
Chat servers (XMPP)
25 IPs ``always on´´
Image transfer servers (HTTPS)
Up to 100 IPs at peak times
Video exchange servers (HTTPS)
Up to 75 IPs at peak times
Audio exchange servers (HTTPS)

## Slide 80
WhatsApp flow characteristics
111
flow throughput
flow size
  Smaller chat/control flows and heavier media flows
  90% chat flows < 10KB
  50% media flows > 70KB
  Only bigger flows considered (>1MB)
  Up to 1.5Mbps in downlink
  Up to 800Kbps in downlink

## Slide 81
WhatsApp flow characteristics and terminal O.S.
111
flow duration (chat flows) [m]
flow duration (mm flows) [m]
timeouts
Blackberry
15 min
Android
10/15/25 min
iOS
3 min
Windows Phone
10 min
Blackberry
15 min
WhatsApp flow characteristics depend on terminal operating system

## Slide 82
111
C. Flow Characteristics and QoE (WhatsApp)
QoE model (download time/MOS)
Laboratory, 50 (27 f, 25m)
23 average age
Experiment
Controlled media file transfer (5MB)
Emulation of different network conditions
(change transfer time)
Users tolerate transfers (in chat apps) of up to 20 seconds with good experience
Threshold of 40 seconds discriminates good and bad experience
The score is independent of the flow size (e.g., independent of video quality)
Laboratory Experiments
Results
Mean Opinion Score (MOS)
from 1 (very bad)
to 5 (excellent)
Distribution of download time (as seen in large-scalepassive traces)
[video exchange in chat application]
From laboratory experiment to operational networks
40% flows last less than 20s (good)
60% flows last less than 40s (acceptable)
35% flows are badly/very badly perceived
Notes: Remove details on model and just put the conclusions and of the model and how they apply

## Slide 83
Measuring QoE through lab experiments
Measurements campaign
50 participants (27 f, 25m)
45/55 male/female
60/40 students/employees
23 average age
Experiment
Media file transfer (5MB)
Emulation of different network conditions
(change transfer time)
Mean Opinion Score (MOS):
From 1 (very bad) to 5 excellent
Users tolerate transfers of up to 20 seconds with good experience
Threshold of 40 seconds discriminates good and bad experience
The score is undependent of the flow size
111
QoE model
transfer time / user score

## Slide 84
From network measurements to QoE estimation
111
40% flows last less than 20s (good)
60% flows last less than 40s (acceptable)
35% flows are badly/very badly perceived
User tests: 5MB transfers, <20s good, >40s bad (previous slide
Assumption: flow size is not taken into account
Apply same model on large scale network traces

## Slide 85
The big WhatsApp outage: Feb. 22nd 2014
111

## Slide 86
The big WhatsApp outage: Feb. 22nd 2014
111
  Drop in volume down
  (with small residual traffic)
  Drop in volume up
  (with small residual traffic)
  Ramp-up on flow counts
  (SYN/RST exchange)
  #whatsappdown
During outage: residual traffic with flow count increase (servers still reachable, failure at application layer)
Clear social media reactions

## Slide 87
Facebook world-wide outage: Sept. 2014
Outages are typically not linked to CDN load-balancing policies
nevertheless, they can still involve the source ASes in different ways
  Drop in Akamai´s volume
1
  Other ASes do not take over
2
  Increase of HTTP 5XX errors
3
  User perceived impairment
4

## Slide 88
Reference Identification Algorithm
111
t0
L(t0) = L0
time
sliding window
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
During normal behavior

## Slide 89
Reference Identification Algorithm
111
t1
L(t1) = L0
time
sliding window
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
During normal behavior

## Slide 90
Reference Identification Algorithm
111
t2
L(t2) = L0
time
sliding window
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
During normal behavior

## Slide 91
Reference Identification Algorithm
111
tm
L(tm) = L0
time
freeze window
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
anomaly start
  Freeze window (avoind including anomaly in the reference
option
#1

## Slide 92
Reference Identification Algorithm
111
tm+1
L(tm+1) = L0
time
freeze window
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
anomaly continues...
  Freeze window (avoind including anomaly in the reference
option
#1

## Slide 93
Reference Identification Algorithm
111
tm+2
L(tm+2) = L0
time
freeze window
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
anomaly continues...
  Freeze window (avoind including anomaly in the reference
option
#1

## Slide 94
Reference Identification Algorithm
111
t?
L(tm+1) = L0
time
freeze window
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
potentially forever
  Freeze window (avoind including anomaly in the reference
option
#1
old reference!

## Slide 95
Reference Identification Algorithm
111
tm
L(tm) = L0
time
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
anomaly start
  Self-adapting window
  (inflating phase)
option
#2
inflate window (right)
rewind...

## Slide 96
Reference Identification Algorithm
111
tm+1
L(tm+1) = L0+1
time
inflate window (right)
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
  Self-adapting window
  (inflating phase)
option
#2

## Slide 97
Reference Identification Algorithm
111
tm+2
L(tm+2) = L0+2
time
inflate window (right)
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
  Self-adapting window
  (inflating phase)
option
#2

## Slide 98
Reference Identification Algorithm
111
tm+3
L(tm+3) = L0+3
time
inflate window (right)
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
  Self-adapting window
  (inflating phase)
option
#2
Hard test
do not include anomalous time-bin in the test

## Slide 99
Reference Identification Algorithm
111
tm+n
L(tm+n) = 2 x L0
time
inflate window (right)
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
  Self-adapting window
  (freeze phase)
option
#2
Soft test
include all time-bins in the test

## Slide 100
Reference Identification Algorithm
111
tk
L(tk) = 2 x L0
time
freeze window and shift
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
  Self-adapting window
  (freeze phase)
option
#2

## Slide 101
Reference Identification Algorithm
111
tk+1
time
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
  Self-adapting window
  (deflate phase)
option
#2
deflate (left) and shift
L(tk+1) = 2 x L0 - 1

## Slide 102
Reference Identification Algorithm
111
tk+2
time
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
  Self-adapting window
  (deflate phase)
option
#2
deflate (left) and shift
L(tk+2) = 2 x L0 - 2

## Slide 103
Reference Identification Algorithm
111
time
L0 = initial window length
L(ti) = window length at ti
t0 = first time-bin
= normal time-bin
t0 = anomalous time-bin
ti
tj
  Self-adapting window
  (back to normal)
option
#2
tn
L(tn) = L0