## Slide 1
Pierdomenico Fiadino
The Telecommunications Research Center Vienna (ftw.)
Vivisecting WhatsApp in Cellular Networks
fiadino@ftw.at
http://userver.ftw.at/~fiadino
Servers, Flows, and Quality of Experience

## Slide 2: WhatsApp overview
Hard facts:
64 billion messages per day
  700 million photos
  100 million videos
500 million of daily active users
Company with the quickest growing user base in history
Acquired by Facebook for 19 billion $
  Each user is worth 40$
Operators need to investigate it because:
It is taking over (or already has...) the SMS/MMS market
They need to learn how to track its usage
They need to understand its impact on their networks

## Slide 3: Outline
Characterization of WhatsApp through hybrid measurements
  Traffic captures in lab with standard tools
  Large-scale passive traces (mobile national network)
  Large-scale active measures (RIPE Atlas)
Quality of Experience remarks
  Build a QoE model with user tests
  Apply model on passive traces
WhatsApp global outage overview
  Characterization
  Social media impact

## Slide 4: Outline
Characterization of WhatsApp through hybrid measurements
  Traffic captures in lab with standard tools
  Large-scale passive traces (mobile national network)
  Large-scale active measures (RIPE Atlas)
Quality of Experience remarks
  Build a QoE model with user tests
  Apply model on passive traces
WhatsApp global outage overview
  Characterization
  Social media impact

## Slide 5: Reverse engineering Whatsapp naming scheme Hybrid measurements
3rd lvl domain
cX, eX, dX
XMPP(5222,443)
media (photo,audio)
prot. (port)
mmiXYZ,mmsXYZ
mmvXYZ
type
media (video)
chat & control
HTTPS (443)
HTTPS (443)
Testbed:
Traffic (chat and media exchange) actively generated at end devices (Android and iOS)
Passively captured at a gateway (Wireshark)
Focus on DNS requests
Android terminal
iOS terminal
Findings:
Whatsapp used custom XMPP protocol
Media exchange via HTTPS servers
One persistent SSL connection to XMPP servers while the app is running
Dedicated TLS connections to HTTPS servers for each media transfer
Servers naming scheme [*.whatsapp.net]:

## Slide 6: Passive probes network architecture
Capture network traces at the core of an operational 3G/4G network (~5 millions of users)
Dataset: 1 month long (February 2014)
Classify flows: only consider Whatsapp-related traffic (details on classification techniques -> next slide)
DBStream
HTTPTag
ISP
network
Internet
Passive probe
<flow,service>
network traces
TCP Flows
metawin monitoring system
Gn interface
HTTP Tickets
DNS requests
TCP statistics
...

## Slide 7: Classification of TCP flows Collect DNS requests from passive traces
Idea: use passively collected DNS requests to dynamically map <services,serverIPs>
resolve: mmi2.whatsapp.net
A: <IP1,IP2,..>, TTL
A: <IP1,IP2,..>, TTL
resolve: c1.whatsapp.net
client #1
client #2
DNS server
Passive probe
Every subsequent flow between a <user> and a <server_ip> in the validity period [validity_start:validity_end] are assigned to <FQDN>
The Fully Qualified Domain Names (FQDN) are assigned to service with usual pattern matching
userID | FQDN | IP | start | end
user #1 | mm2.whatsapp.net | 1.1.1.1 | 14041347 | 14041349
user #2 | c1.whatsapp.net | 2.2.2.2 | 14030424 | 14031288
... | ... | ... | ... | ...
local mapping
validity period (TTL)

## Slide 8: Revealing Hosting Infrastructure Through large-scale passive measurements
386 IP adresses used by Whatsapp (chat and media)
All in AS36351 (Softlayer)
Service/AS | #IPs | # /24 | # /16 | # /8
WhatsApp | 386 | 51 | 30 | 24
SoftLayer (AS36351) | 1364480 | 5330 | 106 | 42

## Slide 9: Revealing Hosting Infrastructure Through large-scale passive measurements
~400 IP addresses in Softlayer AS
Two big steps in RTT distribution at:
  106ms
  114ms
Localized by MaxMind in:
  Houston
  Dallas
Localization of servers through RTT measurements

## Slide 10: Revealing Hosting Infrastructure Through large-scale passive measurements
Active IPs
Chat servers
  150 IPs “always on”
Images exch. servers
  25 IPs “always on”
Video exchange servers
  Up to 100 IPs at peak hours
Audio exchange servers
  Up to 75 IPs at peak hours
At least 200 IP addresses active at any time

## Slide 11: Whatsapp traffic characteristics flow size and throughput
flow throughput
flow size
Smaller chat/control flows and heavier mm flows
90% of chat flows < 10KB
50% of mm flows > 70KB
Only bigger flows (>1MB) considered
Up to 1.5Mbps in downlink
Up to 800Kbps in uplink

## Slide 12: Whatsapp traffic characteristics flow duration with OS breakdown
flow duration (chat flows) [m]
flow duration (mm flows) [m]
Timeouts:
Android: 10/15/25 min
iOS: 3 min
Blackberry: 15 min
Windows Phone: 10 min
Timeouts:
Blackberry: 90 sec
Flow characteristics depend on terminal operating system

## Slide 13: RIPE Atlas infrastructure for geo-distributed active measurements
RIPE NCC: Regional Internet Registry for Europe (equivalent of ARIN for North America)
RIPE Atlas: a large measurement network composed of geographically distributed active probe used to measure connectability and reachabiltiy
RIPE Atlas probe v3
TP-Link MR3020 router with custom firmware
http://atlas.ripe.net

## Slide 14: Hosting infrastructure „stability“ Geographical distributed active measurements
My UDM (User Defined Measurement): 600 probes world-wide resolve Whatsapp hostnames ({mmX|dX}.whatsapp.net)
Result: same set of IP addresses
RIPE Atlas probe v3
TP-Link MR3020 router with custom firmware
http://atlas.ripe.net
Previous conclusions for WhatsApp hosting infrastructure are still valid from other VPs

## Slide 15: Outline
Characterization of WhatsApp through hybrid measurements
  Traffic captures in lab with standard tools
  Large-scale passive traces (mobile national network)
  Large-scale active measures (RIPE Atlas)
Quality of Experience remarks
  Build a QoE model with user tests
  Apply model on passive traces
WhatsApp global outage overview
  Characterization
  Social media impact

## Slide 16: Quality of Experience (QoE) Measuring Mean Opinion Score (MOS) through user tests
Measurement campaign:
50 participants
45/50 male/female
60/40 students/employees
23 average age
Experiment:
Media file transfer (5MB)
Emulation of different network conditions (change transfer time)
Mean Opinion Score (MOS):
From 1 (very bad) to 5 (excellent)
Users tolerate transfers of up to 20 seconds with good experience
Threshold of 40 seconds discriminates good and bad experience
The score is undependent of the flow size

## Slide 17: Quality of Experience (QoE) in the large scale measurements
User tests: 5MB transfers, <20s good, >40s bad (previous slide)
Assumption: flow size is not taken into account
Apply same model on large scale network traces
40% flows last less than 20s (good)
60% flows last less than 40s (acceptable)
35% flows are badly/very badly perceived

## Slide 18: Outline
Characterization of WhatsApp through hybrid measurements
  Traffic captures in lab with standard tools
  Large-scale passive traces (mobile national network)
  Large-scale active measures (RIPE Atlas)
Quality of Experience remarks
  Build a QoE model with user tests
  Apply model on passive traces
WhatsApp global outage overview
  Characterization
  Social media impact

## Slide 19: The big 5-hours outage (Feb. 22nd, 2014) press reaction

## Slide 20: The big outage (Feb. 22nd, 2014) as seen from passive measurements and social feeds
#whatsappdown
drop in volume down
(with small residual traffic)
drop in volume up
(with small residual traffic)
ramp-up on flow counts
(SYN/RST exchange)
Residual traffic during outage
Number of flow increase
Clear social media reactions

## Slide 21: Conclusions
Characterization of WhatsApp
  Hybrid methodology for service characterization
  Revealed *.whatsapp.net server naming scheme
  Centralized infrastructure by Softlayer in Texas
  75% of volume for media transfers (36% is video)
Quality of Experience remarks
  Downlink throughput up to 1.5Mbps, but...
  40% of flows could suffer of bad user experience
WhatsApp global outage overview
  Servers still reachable, fail at app layer
  Strong social media impact ( correlation)

## Slide 22
thank you for you attention!
Pierdomenico Fiadino
Telecommunications Research Center of Vienna (FTW)
<fiadino@ftw.at>
http://www.ftw.at
http://www.ict-mplane.eu
backup slides =>

## Slide 23: The big outage (Feb. 22nd, 2014) as seen from passive measurements and social feeds
residual volume down (mm)
residual volume up (chat)
TCP flags counters