## Slide 1
Pierdomenico Fiadino
The Telecommunications Research Center Vienna (ftw.)
Towards Automatic Detection and Diagnosis of Internet Service Anomalies via DNS Traffic Analysis
fiadino@ftw.at
http://userver.ftw.at/~fiadino

## Slide 2
MOTIVATION
111
RCATool: An Automatic Detection and Diagnosis Framework Slide #2
Today’s Internet is characterized by increasing complexity
Multiple network types (WiFi, cellular, FTTH, etc.)
Large scale and highly distributed services (CDNs)
Sophisticated and highly dynamic traffic patterns
Frequent anomalies involving specific sub-populations of users
Application usage patterns (negatively) impacting cellular signaling
In such a complex scenario,
Anomaly Detection and Diagnosis
is still an open research topic
RCATool: a general framework for automatic detection and diagnosis of application- and device- specific anomalies

## Slide 3
111
PASSIVELY CAPTURED DATASET
cellular network‘s core
internet
DBStream
RCATool
passive probe
network traces
devices
Radio Access Network
RCATool: An Automatic Detection and Diagnosis Framework Slide #3
Results in this paper are based on DNS traffic analysis. Other network traces types are under study.

## Slide 4
DIAGNOSIS FRAMEWORK
111
Symptomatic Signal Extraction
Diagnostic
Signal Extraction
Change Detection Module
Change Detection Module
Network
Traces
(traffic features)
Diagnosis Module
Symptom query_cnt
Diagnostic manufacture
Diagnostic operative_sys
Diagnostic FQDN
Granularity 30 minutes
Warning_start 2015-02-14
Alarm_start 2015-02-14
alarm_end 2015-02-14
Warning_end 2015-02-14
Symptom query_cnt
Diagnostic manufacture
Diagnostic operative_sys
Diagnostic FQDN
Granularity 30 minutes
Warning_start 2015-02-14
Alarm_start 2015-02-14
alarm_end 2015-02-14
Warning_end 2015-02-14
Symptom query_cnt
Diagnostic manufacture
Diagnostic operative_sys
Diagnostic FQDN
Granularity 30 minutes
Warning_start 2015-02-14
Alarm_start 2015-02-14
alarm_end 2015-02-14
Warning_end 2015-02-14
Symptom query_cnt
Diagnostic manufacture
Diagnostic operative_sys
Diagnostic FQDN
Granularity 30 minutes
Warning_start 2015-02-14
Alarm_start 2015-02-14
alarm_end 2015-02-14
Warning_end 2015-02-14
Symptom query_cnt
Diagnostic manufacture
Diagnostic operative_sys
Diagnostic FQDN
Granularity 30 minutes
Warning_start 2015-02-14
Alarm_start 2015-02-14
alarm_end 2015-02-14
Warning_end 2015-02-14
Event Reports
passively collected
(e.g., from a mobile network core)
statistical content of diagnostic-symptomatic traffic features
probability distribution-based algorithm
State management and automatic signal correlation
provide support in troubleshooting of anomalous events
KEY IDEA #1: distinguish between
  symptomatic signals (notify presence of anomalous state) and
  diagnostic signals (provide context)
KEY IDEA #2: observe significant changes in multiple traffic features
KEY IDEA #3: keep status of detected changes and coordinate output
RCATool: An Automatic Detection and Diagnosis Framework Slide #4

## Slide 5
SIGNAL EXTRACTION
111
DNS-based signals
describe statistical content of traffic features
Initial tests: signals based on DNS traffic monitoring
Symptomatic Signals: probability distribution of number of users across query count (i.e., count how many users execute a given number of queries per each time-bin)
Diagnostic Signals: distribution of query count across DNS traffic features (e.g., list of device manufacturer, operating system, hostnames).
manufacturer
number of DNS queries
Apple
Samsung
Huawei
HTC
LG
RCATool: An Automatic Detection and Diagnosis Framework Slide #5

## Slide 6
DETECTION MODULE
111
signal extr.
signal extr.
change
detection
change
detection
traces
diagnosis
RCATool: An Automatic Detection and Diagnosis Framework Slide #6
Based on anomaly detection tool(s) from previous works, improved
Key module for the whole framework
Tested two alternative detection strategies*
* Spoiler alert: one doesn‘t (always) work

## Slide 7
111
111
TRAFFIC FEATURE DISTRIBUTION
manufacturers
number of DNS queries
Apple
Samsung
Huawei
HTC
LG
Distribution of DNS queries across device manufacturer
Devices affected by an anomaly induce a change in traffic feature distributions
RCATool: An Automatic Detection and Diagnosis Framework Slide #7

## Slide 8
111
111
TWO ALTERNATIVE DETECTORS
Represent entire distribution as Entropy
Entropies captures the dispersion of the corresponding probability distribution
A change in traffic patterns induces a change (spike/notch) in the entropy of the relevant traffic feature
Detector #1: Entropy-based
Hf(t0) = 0.42
Entropy
feature f distribution at t0
2015-08-18 08:00
RCATool: An Automatic Detection and Diagnosis Framework Slide #8

## Slide 9
111
TWO ALTERNATIVE DETECTORS
A more complex solution: consider whole empirical distribution of traffic features instead of just its entropy
Compute distance between distribution and a reference set of anomaly-free distributions (rapresenting normal behaviour)
Entropy normalized KL metric
Detector #2: Distribution-based
111
Df(ti) = 3
current distribution at ti
reference distribution r
Distribution distance metric
Kullback-Leibler divergence
RCATool: An Automatic Detection and Diagnosis Framework Slide #9

## Slide 10
111
REAL-WORLD USE CASES
device-specific push/cloud services
?
?
?
?
?
RCATool: An Automatic Detection and Diagnosis Framework Slide #10
RCATool framework evaluated for 6 months in 2014 on operational cellular network (DNS traffic)
Many paradigmatic use-cases (events) have been collected
manufacturers
#DNS queries
operative systems
#DNS queries
DNS
server
requested hostnames (FQDN)
#DNS queries

## Slide 11
111
SEMI-SYNTHETIC DATA GENERATION
RCATool: An Automatic Detection and Diagnosis Framework Slide #11
RCATool framework evaluated for 6 months in 2014 on operational cellular network (DNS traffic)
Many paradigmatic use-cases (events) have been collected
still difficult to perform a complete evaluation...
Generate semi-synthetic background traffic
Over-impose synthetic anomalies

## Slide 12
111
SEMI-SYNTHETIC DATA GENERATION
RCATool: An Automatic Detection and Diagnosis Framework Slide #12
Generation of semi-synthetic data derived from real traffic traces, preserving:
temporal dynamics (24-hours seasonality)
statistical characteristics
working days/Weekends differentiation
Inject additive anomalies in relevant signals:
Alter generated traffic distributions according to models of real-life anomalies
Clean back-ground traffic:
Synthetic anomalies superposition:

## Slide 13
REAL-WORLD USE CASES
111
 | Event #1 | Event #2
Start time | 9:00 | 12:00
Duration | 1 hour | 2 days
Devices | 10% | 5%
Back-off time | 5 seconds | 180 seconds
Manufacturer | Apple Inc. | Multiple (Samsung, HTC, ...)
O.S. | iOS 8.* | Android 4.*
Error flag | +5% time-outs | --
FQDN | OS-specific Top 3LD (push.apple.com) | OS-specific Top 3LD (mtalk.google.com)
RCATool: An Automatic Detection and Diagnosis Framework Slide #13

## Slide 14
DNS TRAFFIC FEATURES
111
DSN traffic features considered
Device related: manufacturer and OS
Service related: requested hostnames (FQDN)
Network performance related: status code of DNS resolver
Anomalies usually visible by observing DNS traffic
Event #1 (Apple)
Event #2 (Android)
RCATool: An Automatic Detection and Diagnosis Framework Slide #14

## Slide 15
DETECTORS OUTPUT
111
Entropy of relevant features is clearly altered
Easily detected by algoriths such as EWMA
Entropy is not clearly visible
EWMA fails to detect the whole duration of the anomaly
Detector #1: Entropy-based
Event #1 (Apple)
Event #2 (Android)
RCATool: An Automatic Detection and Diagnosis Framework Slide #15

## Slide 16
DETECTORS OUTPUT
111
Both event type exhibit a clear devergence from the normality reference
The whole duration of the anomaly is detected
Detector #2: Distribution-based
Event #1 (Apple)
Event #2 (Android)
RCATool: An Automatic Detection and Diagnosis Framework Slide #16

## Slide 17
111
COMPARING PERFORMANCE
Event Type #1
Event Type #2
Entropy-based
detector
Distribution-based
detector
ROC Curves
RCATool: An Automatic Detection and Diagnosis Framework Slide #17

## Slide 18
COMPARING PERFORMANCE
111
Entropy-based detectors are the most popular and largerly adopted, but they fail in coping with smaller-intensity – but still harmful – anomalies which are very common in modern-day networks
RCATool: An Automatic Detection and Diagnosis Framework Slide #18

## Slide 19
DIAGNOSIS MODULE (ONGOING...)
111
Change detection, from state-less to state-full: manage signal change notifications in a state-full fashion (manage change module flipping during long-term events).
diagnosis
Normal
fr = 0
Warning
0 < fr < th
Anomaly
fr ≥ th
Automatic Diagnosis Module
Keep state of the signal changes
Correlate the changes to produce a diagnosis
Signal-specific state machine
Change notifications are kept in a shift register. State transitions depend on fraction fr of anomalous time-bins in the register
Signal change correlation: locate changes in the symptomatic signals, find correlated changes in diagnostic signals to unveil root cause. Manage event termination/mutation.
RCATool: An Automatic Detection and Diagnosis Framework Slide #19

## Slide 20
EVENT REPORT
Event #123456 {Gran. 30 minutes}
-----------------------------------
Symptoms:
* query_cnt [10,+][1,-]
Correlated diagnostic signals:
* manufacturer [Samsung,+]
* operative_sys [Android 4.1.2,+]
* FQDN [youcloud.com,+]
Uncorrelated diagnostic signals:
* error code […]
* APN […]
-----------------------------------
Timestamps:
Warning_start 2015-02-14 13:00
Alarm_start 2015-02-14 13:30
Alarm_end 2015-02-16 11:00
Warning_end 2015-02-16 12:00
increase of users executing
1 query / 3 minuties
Samsung users running Android 4.1.2, resolving youcloud.com
APN independent, error code distribution is not impacted
for almost 2 days
RCATool: An Automatic Detection and Diagnosis Framework Slide #20

## Slide 21
CONCLUSIONS
111as
RCATool: An Automatic Detection and Diagnosis Framework Slide #21
Preliminary study on a framework for automatic and diagnosis of large scale Internet anomalies
Preliminary version is up and running in operational netowrk
Data generation: synthetic traffic distributions for designing and tuning the framework
Ongoing work: expand test-bed with other templates
Comparison of two alternative algorithms for the detector module
Ongoing work: improvements for the distribution-based algorithm
Preliminary diagnosis module for signal coordination and status management
Ongoing work: Machine-Learning approach
1
2
3
4

## Slide 22
Thank you for your attention 
Pierdomenico Fiadino
The Telecommunications Research Center of Vienna
http://userver.ftw.at/~fiadino
fiadino@ftw.at
http://www.ict-mplane.eu/

## Slide 23
backup slides

## Slide 24
CHANGE DETECTION MODULE
111
Challenging Entropy-based Anomaly Detection and Diagnosis Slide #24
Self Adaptive Reference Set Identification: find normality reference from past distributions
Change test: use a normalized variant of the Kullback-Leibler divergence to decide if current distribution is compatible with the reference-set
Changing elements report: notify distribution elements that cause change (e.g., involved hostnames and operating systems)
Statistical Change Detection algorithm
Recognize macroscopic deviations in distributions
Algorithm consists of three phases for each iteration:
x1 and x2 are similar → KLd(x1,x2) is small
x1 and x3 are dissimilar → KLd(x1,x3) is large
feature
CDF
x1
x2
x3